## Slide 1: Souk-up Algorithm
Mini project 2
Made by: Habiba Gamal

## Slide 2: Background
Fast Maze Router
Builds upon Lee’s algorithm
Does not guarantee an optimum route as in Lee’s
Runs 10-50 times faster than Lee’s Algorithm
Complexity: O(NxM)

## Slide 3: Assumptions
Initially, the grid is empty
Initial routes remain on the grid for later routes (act as obstacles)
There are only 3 available metal layers (M1: horizontal, M2: vertical, M3: horizontal)
Vias can be placed anywhere on the grid
Vias have cost that is a user input at the beginning of the program
The source and target cells can be non-empty cells (part of previous routes)

## Slide 4: 4 implementation variants
Classical Implementation
2) Classical Implementation with Swap if no path
3) Flood less
4) Flood less with swap

## Slide 5: 1) Classical implementation
Create a wire from the source in the direction of the target until:
1) an obstacle is hit,
2) or if in a vertical metal layer, x coordinate of the target passed
3) or if in a horizontal metal layer, y coordinate of the target passed
Start flooding from the obstacle until the target is hit

## Slide 6: 2) Classical implementation w/ swap
Same as implementation 1.
Difference: If no path is found, the coordinates of the target and the source are swapped and the algorithm is repeated again to find a path

## Slide 7: 3) Floodless
Create a wire from the source in the direction of the target until:
1) an obstacle is hit,
2) or if in a vertical metal layer, x coordinate of the target passed
3) or if in a horizontal metal layer, y coordinate of the target passed
Then move to another metal layer and do the same thing
Start flooding only when there is no way you can create a wire from source to target

## Slide 8: 4) Floodless with swap
Same as implementation 3
Difference: when there is no path, the coordinates of the source and target are swapped and the algorithm is repeated

## Slide 9: Expected differences between variants
Implementations with swaps take longer execution time than implementations without swaps
Floodless take less execution time than classical implementation
Implementations with swaps generate better output that implementations without swaps
Floodless generate worse outputs than classical implementation

## Slide 10: Actual differences between Variants
Floodless takes less time to execute than classical implementation. This is showcased in testcases 5 and 6.
Testcases 5 and 6 are the same inputs, but 5 is using floodless and 6 is not. The execution time for 5 is way faster than 6.

## Slide 11: Actual differences between Variants (Cont’d)
Swapping does not yield significantly better results than not swapping.
This can be shown in testcases 7 and 8. In testcase 7, swapping was enabled. In testcase 8, swapping was disabled. However, for both testcases, the same inputs yielded no path available whether swapping was on or not.
Similarly, in testcases 9 & 10. In testcase 9, swapping was enabled. In testcase 10, swapping was disabled. The same inputs generated no path available in both cases.
Swapping source and target does not generate significant difference from not swapping source and target.

## Slide 12: Actual differences between Variants (Cont’d)
Floodless does not generate worse results than classical implementation. For all the tried testcases, the route cost from floodless is the same as the route cost without floodless.
Floodless did not affect the availability of routes in any of the testcases.
This can be shown in testcase 11 (floodless was on). When compared to testcases 9 & 10 (floodless was off), the same route costs were generated, and the same inputs yielded no path available in all 3 testcases.

## Slide 13: Conclusion
Swapping source and target to find alternative path when there is no path available does not generate significant difference and thus can be ignored and not implemented.
Floodless did not generate significant difference when it comes to route cost and congestion. However, it generated significant difference when it comes to CPU time. Execution time with floodless on is way less than execution time with floodless off. Floodless is worth implementing.